Sample solutions

1a. Characteristic of the supersonic microphones

(Amplitude of input signal is 1 V, constant).

| f, Hz | U,V | U/Umax |
| --- | --- | --- |
| 38600 | 155 | 0.168 |
| 39000 | 245 | 0.266 |
| 39400 | 470 | 0.511 |
| 39800 | 830 | 0.902 |
| 39850 | 865 | 0.940 |
| 39900 | 895 | 0.973 |
| 40000 | 915 | 0.995 |
| 40020 | 910 | 0.989 |
| 40100 | 885 | 0.962 |
| 40200 | 820 | 0.891 |
| 40400 | 660 | 0.717 |
| 40600 | 470 | 0.511 |
| 40800 | 300 | 0.326 |
| 41000 | 205 | 0.223 |
| 41200 | 144 | 0.157 |
| 41300 | 125 | 0.136 |
| 41400 | 110 | 0.120 |

Fig 2. Characteristic of super sonic microphone. Amplitude of input signal 1V.

The microphones system of source and detector’s is high sensitivity in the range frequency  .

Amplifier amplified signal in the range frequency 10 kHz- 200 kHz.

1b. Dependence amplitude emitted signal of angle

| angle, degree | Amplitude of signal U, mV | U/Umax | angle, degree | Amplitude of signal U, mV | U/Umax |
| --- | --- | --- | --- | --- | --- |
| 0 | 300 | 1 | 250 | 30 | 0.10 |
| 10 | 280 | 0.93 | 260 | 33 | 0.11 |
| 20 | 260 | 0.87 | 270 | 32 | 0.11 |
| 30 | 200 | 0.67 | 280 | 52 | 0.17 |
| 40 | 150 | 0.50 | 290 | 65 | 0.22 |
| 50 | 120 | 0.40 | 300 | 100 | 0.33 |
| 60 | 100 | 0.33 | 310 | 120 | 0.40 |
| 70 | 68 | 0.23 | 320 | 150 | 0.50 |
| 80 | 50 | 0.17 | 330 | 200 | 0.67 |
| 90 | 30 | 0.10 | 340 | 260 | 0.87 |
| 100 | 30 | 0.10 | 350 | 280 | 0.93 |
| 110 | 30 | 0.10 | 360 | 300 | 1.00 |

| angle | U, V | U/Umax | angle | U, V | U/Umax |
| --- | --- | --- | --- | --- | --- |
| 5 | 0.68 | 1 | 180 | 0.068 | 0.100 |
| 10 | 0.66 | 0.971 | 210 | 0.038 | 0.056 |
| 20 | 0.62 | 0.912 | 240 | 0.034 | 0.050 |
| 30 | 0.55 | 0.809 | 250 | 0.046 | 0.068 |
| 40 | 0.45 | 0.662 | 270 | 0.082 | 0.121 |
| 50 | 0.365 | 0.537 | 300 | 0.245 | 0.360 |
| 60 | 0.26 | 0.382 | 330 | 0.53 | 0.779 |
| 70 | 0.18 | 0.265 | 335 | 0.57 | 0.838 |
| 80 | 0.105 | 0.154 | 340 | 0.6 | 0.882 |
| 90 | 0.072 | 0.106 | 345 | 0.64 | 0.941 |
| 100 | 0.08 | 0.118 | 350 | 0.66 | 0.971 |
| 120 | 0.095 | 0.140 | 355 | 0.68 | 1.000 |
| 150 | 0.014 | 0.021 | 360 | 0.68 | 1.000 |

Part 2. Interference of Wave.

2a. Observation the Interference of Ultra Sound Wave.

Fill the table ( Correct or Incorrect ).

| a | b | c | d | e | f | g |
| --- | --- | --- | --- | --- | --- | --- |
| ( | X | X | ( | X | ( | ( |

a) and b) The resultant standing wave y equation will be the sum of y1 and y2:

Using a trigonometric identity to simplify, the standing wave is described by:

c) In the positions A we can observe standing wave, but in the positions B only detects reflected waves.

e)

f) and g)

2b. Determination the Wavelength.

| № | , mm |  | n, number of antinodes in SM | , mm |
| --- | --- | --- | --- | --- |
| 0 | 29.5 | 6.88 | 7 | -0.53 |
| 1 | 34.5 | 8.04 | 8 | 0.18 |
| 2 | 38.5 | 8.97 | 9 | -0.11 |
| 3 | 42.5 | 9.91 | 10 | -0.40 |
| 4 | 47.5 | 11.07 | 11 | 0.31 |
| 5 | 51.5 | 12.00 | 12 | 0.02 |
| 6 | 56 | 13.05 | 13 | 0.23 |
| 7 | 60.5 | 14.10 | 14 | 0.44 |
| 8 | 64.5 | 15.03 | 15 | 0.15 |
| 9 | 69 | 16.08 | 16 | 0.36 |
| 10 | 73 | 17.02 | 17 | 0.07 |
| 11 | 77.6 | 18.09 | 18 | 0.38 |
| 12 | 81.5 | 19.00 | 19 | -0.01 |
| 13 | 86 | 20.05 | 20 | 0.20 |
| 14 | 90 | 20.98 | 21 | -0.09 |
| 15 | 94.5 | 22.03 | 22 | 0.12 |
| 16 | 99.2 | 23.12 | 23 | 0.53 |
| 17 | 103 | 24.01 | 24 | 0.04 |
| 18 | 108 | 25.17 | 25 | 0.75 |
|  |  |  | average | 0.14 |
|  |  |  | abs dev | 0.23 |

From graph,

Theoretically

2c. Observation the Standing Wave.

Fill the tables by marks ANT (antinode) or NODE (node) for the observed standing wave.

- On the surface of the mirror

| Detection signal level | On the surface of the mirror | Expression |
| --- | --- | --- |
| Maximal | Node | Mirror is closed end |
| Minimal | Node | Mirror is closed end |

- On the surface of the source

| Detection signal level | On the surface of the source | Expression |
| --- | --- | --- |
| Maximal | Antinode | See Figure D1 |
| Minimal | Node | See Figure D2 |

Figure D1

Figure D2

3. The Doppler effect

Make an adjustment of instrument for the measurement the Doppler effect from the side of disk, observe effect.

3a. Write formula

Mirror receding:  ;

Mirror approaching:  ;

Solution: In this situation there two Doppler shifts. In the first shift, the mirror is the receding “Receiver”.

The frequency of sound reaching the mirror

In the second shift, the mirror acts as a source of sound with frequency , and the receiver is the Detector.

The frequency of sound reaching the detector

Then the frequency measured by the detector is

3b. Simple formula

Oder solutions:

| 3a1. Angular incidence and angular detecting |  |
| --- | --- |
| Solution: |  |
| Simple formula |  |
| 3a2. Normal incidence and normal detecting |  |
| Mirror receding Mirror approaching |  |
| 3a2. Normal incidence, angular detecting |  |
| 3a3. Angular incidence, same angular detecting |  |
| Solution: |  |

| 3a4. Incidence and detecting to direction centre of the circle. |  |
| --- | --- |
| Solution: |  |
| Angle, degree 0 5 10 15 20 25 Cos(angle) 1.00 0.996 (0.4 %) 0.985 (1.5 %) 0.966 (3.4 %) 0.940 (6%) 0.906 (10 %) |

3c. Experiment.  The Doppler effect.

3c1.    Tabulete                          (Direction of rotation of the disk: decreasing frequency)

| № | Voltage U (V) | Current I (A) | Output frequency f (Hz) | Input frequency (Hz) | (Hz) |  |  | Power P=I*U (W) | Impedance Z=U/I (Ohm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 16 | 1.23 | 38705 | 40000 | 1295 | 3.24E-02 | 2.06E-03 | 19.68 | 13.01 |
| 2 | 15 | 1.15 | 38772 | 40000 | 1228 | 3.07E-02 | 2.08E-03 | 17.25 | 13.04 |
| 3 | 14 | 1.08 | 38853 | 40000 | 1147 | 2.87E-02 | 2.09E-03 | 15.12 | 12.96 |
| 4 | 13 | 1 | 38915 | 40000 | 1085 | 2.71E-02 | 2.13E-03 | 13 | 13.00 |
| 5 | 12 | 0.9 | 38997 | 40000 | 1003 | 2.51E-02 | 2.13E-03 | 10.8 | 13.33 |
| 6 | 11 | 0.81 | 39081 | 40000 | 919 | 2.30E-02 | 2.14E-03 | 8.91 | 13.58 |
| 7 | 10 | 0.73 | 39154 | 40000 | 846 | 2.12E-02 | 2.17E-03 | 7.3 | 13.70 |
| 8 | 9 | 0.61 | 39249 | 40000 | 751 | 1.88E-02 | 2.15E-03 | 5.49 | 14.75 |
| 9 | 8 | 0.54 | 39339 | 40000 | 661 | 1.65E-02 | 2.13E-03 | 4.32 | 14.81 |
| 10 | 7 | 0.48 | 39418 | 40000 | 582 | 1.46E-02 | 2.16E-03 | 3.36 | 14.58 |
| 11 | 6.5 | 0.44 | 39473 | 40000 | 527 | 1.32E-02 | 2.11E-03 | 2.86 | 14.77 |
| 12 | 6 | 0.43 | 39500 | 40000 | 500 | 1.25E-02 | 2.17E-03 | 2.58 | 13.95 |
| 13 | 5.5 | 0.39 | 39549 | 40000 | 451 | 1.13E-02 | 2.15E-03 | 2.145 | 14.10 |
| 14 | 5 | 0.38 | 39583 | 40000 | 417 | 1.04E-02 | 2.19E-03 | 1.9 | 13.16 |
| 15 | 4.5 | 0.36 | 39630 | 40000 | 370 | 9.25E-03 | 2.18E-03 | 1.62 | 12.50 |
| 16 | 4 | 0.33 | 39674 | 40000 | 326 | 8.15E-03 | 2.17E-03 | 1.32 | 12.12 |
| 17 | 3.5 | 0.31 | 39723 | 40000 | 277 | 6.93E-03 | 2.13E-03 | 1.085 | 11.29 |
| 18 | 3 | 0.3 | 39758 | 40000 | 242 | 6.05E-03 | 2.20E-03 | 0.9 | 10.00 |
| 19 | 2.5 | 0.28 | 39800 | 40000 | 200 | 5.00E-03 | 2.22E-03 | 0.7 | 8.93 |
| 20 | 2 | 0.26 | 39847 | 40000 | 153 | 3.83E-03 | 2.19E-03 | 0.52 | 7.69 |
| 21 | 1.5 | 0.25 | 39887 | 40000 | 113 | 2.83E-03 | 2.26E-03 | 0.375 | 6.00 |
| (-) | 1 | 0.24 | 39936 | 40000 | 64 | 1.60E-03 | 2.13E-03 | 0.24 | 4.17 |
| (-) | 0.5 | 0.24 | 39973 | 40000 | 27 | 6.75E-04 | 2.70E-03 | 0.12 | 2.08 |
|  | Threshold of motion | Average (N1:N21) | 2.15E-03 |  |  |
|  |  |  | Abs error | 3.70E-05 |  |  |

From graph,

(2)

(Direction of rotation of the disk: decreasing frequency)

3c. Experiment.  The Doppler effect.

Tabulete                          (Direction of rotation of the disk: decreasing frequency)

| № | Voltage U (V) | Current I (A) | Output frequency f (Hz) | Input frequency (Hz) | (Hz) |  |  | Power P=I*U (W) | Impedance Z=U/I (Ohm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 16 | 1.23 | 38705 | 40000 | 1295 | 3.24E-02 | 2.06E-03 | 19.68 | 13.01 |
| 2 | 15 | 1.15 | 38772 | 40000 | 1228 | 3.07E-02 | 2.08E-03 | 17.25 | 13.04 |
| 3 | 14 | 1.08 | 38853 | 40000 | 1147 | 2.87E-02 | 2.09E-03 | 15.12 | 12.96 |
| 4 | 13 | 1 | 38915 | 40000 | 1085 | 2.71E-02 | 2.13E-03 | 13 | 13.00 |
| 5 | 12 | 0.9 | 38997 | 40000 | 1003 | 2.51E-02 | 2.13E-03 | 10.8 | 13.33 |
| 6 | 11 | 0.81 | 39081 | 40000 | 919 | 2.30E-02 | 2.14E-03 | 8.91 | 13.58 |
| 7 | 10 | 0.73 | 39154 | 40000 | 846 | 2.12E-02 | 2.17E-03 | 7.3 | 13.70 |
| 8 | 9 | 0.61 | 39249 | 40000 | 751 | 1.88E-02 | 2.15E-03 | 5.49 | 14.75 |
| 9 | 8 | 0.54 | 39339 | 40000 | 661 | 1.65E-02 | 2.13E-03 | 4.32 | 14.81 |
| 10 | 7 | 0.48 | 39418 | 40000 | 582 | 1.46E-02 | 2.16E-03 | 3.36 | 14.58 |
| 11 | 6.5 | 0.44 | 39473 | 40000 | 527 | 1.32E-02 | 2.11E-03 | 2.86 | 14.77 |
| 12 | 6 | 0.43 | 39500 | 40000 | 500 | 1.25E-02 | 2.17E-03 | 2.58 | 13.95 |
| 13 | 5.5 | 0.39 | 39549 | 40000 | 451 | 1.13E-02 | 2.15E-03 | 2.145 | 14.10 |
| 14 | 5 | 0.38 | 39583 | 40000 | 417 | 1.04E-02 | 2.19E-03 | 1.9 | 13.16 |
| 15 | 4.5 | 0.36 | 39630 | 40000 | 370 | 9.25E-03 | 2.18E-03 | 1.62 | 12.50 |
| 16 | 4 | 0.33 | 39674 | 40000 | 326 | 8.15E-03 | 2.17E-03 | 1.32 | 12.12 |
| 17 | 3.5 | 0.31 | 39723 | 40000 | 277 | 6.93E-03 | 2.13E-03 | 1.085 | 11.29 |
| 18 | 3 | 0.3 | 39758 | 40000 | 242 | 6.05E-03 | 2.20E-03 | 0.9 | 10.00 |
| 19 | 2.5 | 0.28 | 39800 | 40000 | 200 | 5.00E-03 | 2.22E-03 | 0.7 | 8.93 |
| 20 | 2 | 0.26 | 39847 | 40000 | 153 | 3.83E-03 | 2.19E-03 | 0.52 | 7.69 |
| 21 | 1.5 | 0.25 | 39887 | 40000 | 113 | 2.83E-03 | 2.26E-03 | 0.375 | 6.00 |
| (-) | 1 | 0.24 | 39936 | 40000 | 64 | 1.60E-03 | 2.13E-03 | 0.24 | 4.17 |
| (-) | 0.5 | 0.24 | 39973 | 40000 | 27 | 6.75E-04 | 2.70E-03 | 0.12 | 2.08 |
|  | Threshold of motion | Average (N1:N21) | 2.15E-03 |  |  |
|  |  |  | Abs error | 3.70E-05 |  |  |

From graph,

(2)

(Direction of rotation of the disk: decreasing frequency)

3d.  Dynamic of the motor

| speed | voltage | Impedance Z | The electrical power | The mechanical power | The dynamic equilibrium |
| --- | --- | --- | --- | --- | --- |
| low speed | low voltage |  |  | -rotation speed of motor -torque of friction force (constant) | (linear) |
| High speed | High voltage |  |  | -torque of fluid resistance | (linear) |
| Result |  |  |  |

3e.

3e1. Function  и .

(3)

3e2.

Given Data:

A). In direction frequency decreasing

for  and

(In direction frequency decreasing)

3f. Determine Sound velocity in air

- Direction of rotation of the disk: decreasing frequency)

(1)

(2)

(3)

from (1)-(3)

3g. Calculate and Observe Double Doppler effect

.   .   .

In direction frequency decreasing

for  and

Measured Doppler effect

4. threshold and resolving power of hearing

|  | Lower limit of hearing | Higher limit of hearing |
| --- | --- | --- |
|  | 17-50 Hz | 12 kHz -20 kHz |

Ижилхэн сонсголын босготой давтамжийн утгууд

| Давтамжийн доод утга | Давтамжийн дээд утга |
| --- | --- |
| 1000 Hz | 8800 Hz |
| 2000 Hz | 8000 Hz |
| 2300 Hz | 7800 Hz |
| 2500 Hz | 7000 Hz |
| 2700 Hz | 6100 Hz |
| 2900 Hz | 5500 Hz |
| Хамгийн сайн сонсогдох давтамжийн завсар буюу сонсголын босгоны минимум |

Resolving power

| Frequency, | Ялгаж байгаа давтамж | Ялгах чадвар | Speed of mirror for detected motion |
| --- | --- | --- | --- |
|  |  | 230 -300 | 0.6-0.7 m/s |
|  |  | 140- 180 | 1-1.2 m/s |
|  |  | 80- 110 | 1.6 -2.0 m/s |

Calculation formule slope and error

.

To calculate the gradient, the following equation was used, where N is the number of data points:

To calculate the standard deviation sY of the individual Y data values, the following equation was used:

Hence the standard deviation in the slope can be calculated: