DIFFERENTIAL THERMOMETRIC METHOD

In this problem, we use the differential thermometric method to fulfill the two following tasks:

1. Finding the temperature of solidification of a crystalline solid substance.

2. Determining the efficiency of a solar cell.

A. Differential thermometric method

In this experiment forward biased silicon diodes are used as temperature sensors to measure temperature. If the electric current through the diode is constant, then the voltage drop across the diode depends on the temperature according to the relation

(1)

where and are respectively the voltage drops across the diode at temperature  and at room temperature  (measured in oC), and the factor

2.00 ( 0.03 mV/ oC										    (2)

The value of may vary slightly from diode to diode.

If two such diodes are placed at different temperatures, the difference between the temperatures can be measured from the difference of the voltage drops across the two diodes. The difference of the voltage drops, called the differential voltage, can be measured with high precision; hence the temperature difference can also be measured with high precision. This method is called the differential thermometric method.	 The electric circuit used with the diodes in this experiment is shown in Figure 1. Diodes D1 and D2 are forward biased by a 9V battery, through 10 k( resistors,  and . This circuit keeps the current in the two diodes approximately constant.

If the temperature of diode D1 is  and that of D2 is , then according to (1), we have:

and

The differential voltage is:

(3)

in which . By measuring the differential voltage , we can determine the temperature difference.

To bias the diodes, we use a circuit box, the diagram of which is shown in Figure 2.

The circuit box contains two biasing resistors of 10 kΩ for the diodes, electrical leads to the 9 V battery, sockets for connecting to the diodes D1 and D2, and sockets for connecting to digital multimeters to measure the voltage drop  on diode D2 and the differential voltage of the diodes D1 and D2.

B. Task 1: Finding the temperature of solidification of a crystalline substance

1. Aim of the experiment

If a crystalline solid substance is heated to the melting state and then cooled down, it solidifies at a fixed temperature , called temperature of solidification, also called the melting point of the substance. The traditional method to determine  is to follow the change in temperature with time during the cooling process. Due to the fact that the solidification process is accompanied by the release of latent heat of phase transition, the temperature of the substance does not change while the substance is solidifying. If the amount of the substance is large enough, the time interval in which the temperature remains constant is rather long, and one can easily determine this temperature. On the contrary, if the amount of substance is small, this time interval is too short to be observed and hence it is difficult to determine .

In order to determine  in case of small amount of substance, we use the differential thermometric method, whose principle can be summarized as follows. We use two identical small dishes, one containing a small amount of the substance to be studied, called the sample dish, and the other not containing the substance, called the reference dish. The two dishes are put on a heat source, whose temperature varies slowly with time. The thermal flows to and from the two dishes are nearly the same. Each dish contains a temperature sensor (a forward biased silicon diode). While there is no phase change in the substance, the temperature of the sample dish and the temperature of the reference dish vary at nearly the same rate, and thus varies slowly with . If there is a phase change in the substance, and during the phase change does not vary and equals , while steadily varies, then varies quickly. The plot of versus shows an abrupt change. The value of corresponding to the abrupt change of  is indeed .

The aim of this experiment is to determine the temperature of solidification  of a pure crystalline substance, having  in the range from 50oC to 70oC, by using the traditional and differential thermal analysis methods. The amount of substance used in the experiment is about 20 mg.

2. Apparatus and materials

1. The heat source is a 20 W halogen lamp.

2. The dish holder is a bakelite plate with a square hole in it. A steel plate is fixed on the hole. Two small magnets are put on the steel plate.

3. Two small steel dishes, each contains a silicon diode soldered on it. One dish is used as the reference dish, the other - as the sample dish.

Each dish is placed on a magnet. The magnetic force maintains the contact between the dish, the magnet and the steel plate. The magnets also keep a moderate thermal contact between the steel plate and the dishes.

A grey plastic box used as a cover to protect the dishes from the outside influence.

Figure 3 shows the arrangement of the dishes and the magnets on the dish holder and the light bulb.

4. Two digital multimeters are used as voltmeters. They can also measure room temperature by turning the Function selector to the ‘’oC/oF” function. The voltage function of the multimeter has an error of (2 on the last digit.

Note: to prevent the multimeter (see Figure 9) from going into the “Auto power off” function, turn the Function selector from OFF position to the desired function while pressing and holding the SELECT button.

5. A circuit box as shown in Figure 2.

6. A 9 V battery.

7. Electrical leads.

8. A small ampoule containing about 20 mg of the substance to be measured.

9. A stop watch

10. A calculator

11. Graph papers.

3. Experiment

1. The magnets are placed on two equivalent locations on the steel plate. The reference dish and the empty sample dish are put on the magnets as shown in the Figure 4. We use the dish on the left side as the reference dish, with diode D1 on it (D1 is called the reference diode), and the dish on the right side as the sample dish, with diode D2 on it (D2 is called the measuring diode).

Put the lamp-shade up side down as shown in Figure 5. Do not switch the lamp on. Put the dish holder on the lamp. Connect the apparatuses so that you can measure the voltage drop on the diode D2, that is , and the differential voltage.

In order to eliminate errors due to the warming up period of the instruments and devices, it is strongly recommended that the complete measurement circuit be switched on for about 5 minutes before starting real experiments.

1.1. Measure the room temperature  and the voltage drop  across diode D2 fixed to the sample dish, at room temperature .

1.2. Calculate the voltage drops ,  and  on the measuring diode at temperatures 50oC, 70oC and 80oC, respectively.

2. With both dishes still empty, switch the lamp on. Follow Vsam. When the temperature of the sample dish reaches ~ 80oC, switch the lamp off.

2.1. Wait until ~ 70oC, and then follow the change in  and  with time, while the steel plate is cooling down. Note down the values of and  every 10 s to 20 s in a table. If  varies quickly, the time interval between consecutive measurements may be shorter. When the temperature of the sample dish decreases to ~ 50oC, the measurement is stopped.

2.2. Plot the graph of versus t, called Graph 1, on a graph paper provided.

2.3. Plot the graph of versus , called Graph 2, on a graph paper provided.

Note: for 2.2 and 2.3 do not forget to write down the correct name of each graph.

3. Pour the substance from the ampoule into the sample dish. Repeat the experiment identically as mentioned in section 2.

3.1. Write down the data of and with time t in a table.

3.2. Plot the graph of versus t, called Graph 3, on a graph paper provided.

3.3. Plot the graph of versus , called Graph 4, on a graph paper provided.

Note: for 3.2 and 3.3 do not forget to write down the correct name of each graph.

4. By comparing the graphs in section 2 and section 3, determine the temperature of solidification of the substance.

4.1. Using the traditional method to determine : by comparing the graphs of versus t in sections 3 and 2, i.e. Graph 3 and Graph 1, mark the point on Graph 3 where the substance solidifies and determine the value  (corresponding to this point) of .

Find out the temperature of solidification  of the substance and estimate its error.

4.2. Using the differential thermometric method to determine : by comparing the graphs of versus  in sections 3 and 2, i.e. Graph 4 and Graph 2, mark the point on Graph 4 where the substance solidifies and determine the value of .

Find out the temperature of solidification  of the substance.

4.3. From errors of measurement data and instruments, calculate error of  obtained with the differential thermometric method. Write down the error calculations and finally write down the values of  together with its error in the answer sheet.

C. Task 2: Determining the efficiency of a solar cell under illumination of an incandescent lamp

1. Aim of the experiment

The aim of the experiment is to determine the efficiency of a solar cell under illumination of an incandescent lamp. Efficiency is defined as the ratio of the electrical power that the solar cell can supply to an external circuit, to the total radiant power received by the cell. The efficiency depends on the incident radiation spectrum. In this experiment the radiation incident to the cell is that of an incandescent halogen lamp. In order to determine the efficiency of the solar cell, we have to measure the irradiance  at a point situated under the lamp, at a distance d from the lamp along the vertical direction, and the maximum power Pmax of the solar cell when it is placed at this point. In this experiment, d = 12 cm  (Figure 6). Irradiance  can be defined by:

in which  is the radiant flux (radiant power), and  is the area of the illuminated surface.

2. Apparatus and materials

1. The light source is a 20W halogen lamp.

2. The radiation detector is a hollow cone made of copper, the inner surface of it is blackened with soot (Figure 7). The cone is incompletely thermally isolated from the surrounding. In this experiment, the detector is considered an ideal black body. To measure temperature, we use silicon diodes. The measuring diode is fixed to the radiation detector (D2 in Figure 1 and Figure 7), so that its temperature equals that of the cone. The reference diode is placed on the inner side of the wall of the box containing the detector; its temperature equals that of the surrounding. The total heat capacity of the detector (the cone and the measuring diode) is . The detector is covered by a very thin polyethylene film; the radiation absorption and reflection of which can be neglected.

3. A circuit box as shown in Figure 2.

4. A piece of solar cell fixed on a plastic box (Figure 8). The area of the cell includes some metal connection strips. For the efficiency calculation these strips are considered parts of the cell.

5. Two digital multimeters. When used to measure the voltage, they have a very large internal resistance, which can be considered infinitely large. When we use them to measure the current, we cannot neglect their internal resistance. The voltage function of the multimeter has an error of (2 on the last digit. The multimeters can also measure the room temperature.

Note: to prevent the multimeter (see Figure 9) from going into the “Auto power off” function, turn the Function selector from OFF position to the desired function while pressing and holding the SELECT button.

6. A 9 V battery

7. A variable resistor.

8. A stop watch

9. A ruler with 1mm divisions

10. Electrical leads.

11. Graph papers.

3. Experiment

When the detector receives energy from radiation, it heats up. At the same time, the detector loses its heat by several mechanisms, such as thermal conduction, convection, radiation etc...Thus, the radiant energy received by detector in a time interval dt is equal to the sum of the energy needed to increase the detector temperature and the energy transferred from the detector to the surrounding:

where  is the heat capacity of the detector and the diode,  - the temperature increase and  - the heat loss.

When the temperature difference between the detector and the surrounding  is small, we can consider that the heat  transferred from the detector to the surrounding in the time interval is approximately proportional to and , that is , with  being a factor having the dimension of W/K. Hence, assuming that  is constant and  is small, we have:

or    											(4)

The solution of this differential equation determines the variation of the temperature difference with time t, from the moment the detector begins to receive the light with a constant irradiation, assuming that at t=0, =0

(5)

When the radiation is switched off, the mentioned above differential equation becomes

(6)

and the temperature difference varies with the time according to the following formula:

(7)

where  is the temperature difference at  (the moment when the measurement starts).

1. Determine the room temperature .

2. Compose an electric circuit comprising the diode sensors, the circuit box and the multimeters to measure the temperature of the detector.

In order to eliminate errors due to the warming up period of the instruments and devices, it is strongly recommended that the complete measurement circuit be switched on for about 5 minutes before starting real experiments.

2.1. Place the detector under the light source, at a distance of d = 12 cm to the lamp. The lamp is off. Follow the variation of for about 2 minutes with sampling intervals of 10 s and determine the value of  in equation (3).

2.2. Switch the lamp on to illuminate the detector. Follow the variation of . Every 10-15 s, write down a value of  in the table provided in the answer sheet. (Note: columns x and y of the table will be used later in section 4.). After 2 minutes, switch the lamp off.

2.3. Move the detector away from the lamp. Follow the variation of for about 2 minutes after that. Every 10-15 s, write down a value of  in the table provided in the answer sheet. (Note: columns x and y of the table will be used later in section 3.).

Hints:

As the detector has a thermal inertia, it is recommended not to use some data obtained immediately after the moment the detector begins to be illuminated or ceases to be illuminated.

3. Plot a graph in an x-y system of coordinates, with variables x and y chosen appropriately, in order to prove that after the lamp is switched off, equation (7) is satisfied.

3.1. Write down the expression for variables x and y.

3.2. Plot a graph of y versus x, called Graph 5.

3.3. From the graph, determine the value of .

4. Plot a graph in an x-y system of coordinates, with variables x and y chosen appropriately, in order to prove that when the detector is illuminated, equation (5) is satisfied.

4.1. Write down the expressions for variables x and y.

4.2. Plot a graph of y versus x, called Graph 6.

4.3. Determine the irradiance E at the orifice of the detector.

5. Put the solar cell to the same place where the radiation detector was. Connect the solar cell to an appropriate electric circuit comprising the multimeters and a variable resistor which is used to change the load of the cell. Measure the current in the circuit and the voltage on the cell at different values of the resistor.

5.1. Draw a diagram of the circuit used in this experiment.

5.2. By rotating the knob of the variable resistor, you change the value of the load. Note the values of current  and voltage  at each position of the knob.

5.3. Plot a graph of the power of the cell, which supplies to the load, as a function of the current through the cell. This is Graph 7.

5.4. From the graph deduce the maximum power Pmax of the cell and estimate its error.

5.5. Write down the expression for the efficiency of the cell that is corresponding to the obtained maximum power. Calculate its value and error.

Contents of the experiment kit (see also Figure 10)

| 1 | Halogen lamp 220 V/ 20 W | 9 | Stop watch |
| --- | --- | --- | --- |
| 2 | Dish holder | 10 | Calculator |
| 3 | Dish | 11 | Radiation detector |
| 4 | Multimeter | 12 | Solar cell |
| 5 | Circuit box | 13 | Variable resistor |
| 6 | 9 V battery | 14 | Ruler |
| 7 | Electrical leads | 15 | Box used as a cover |
| 8 | Ampoule with substance to be measured |  |  |

Note: to prevent the multimeter (see Figure 9) from going into the “Auto power off” function, turn the Function selector from OFF position to the desired function while pressing and holding the SELECT button.

# Text boxes

Function selector

Figure 9. Digital multimeter

diode D1

D2

Cover

Red

Blue

Black

8

9 V

ΔV

V2

Black

d = 12 cm

Red

Figure 5

Using the halogen lamp as a heat source

Figure 6

Using the halogen lamp

as a light source

12

10

D2

Figure 3. Apparatus for measuring the solidification temperature

D1

Sample dish

Ref. dish

12V/20W bulb

Blue

10 k(

Red

Figure 8

Solar cell

Black

Select

s

Magnet

Steel plate

9

D1

Reference

Red

10 k(

Common- Black

To D1 - Blue

To D2 - Red

Figure 2. Diagram of the circuit box

(top view)

Red

11

Figure 7. Diagram of the radiation detector

Figure 1. Electric circuit of the diode sensors

Blue

Figure 4. The dishes on the dish holder (top view)

Black

Common

Black

14

13

Blue

Red

6

5

7

diode D2

Measuring

Thermal insulator

Figure 10. Contents of the experiment kit

15

4

3

2

1